## Slide 1
Security Gate with Online Key, QR Code & RFID
SMARTGATE
Smart IoT-Based Ticketing & Access Control

## Slide 2
INTRODUCTION
SmartGate is an IoT-powered security gate system that combines QR code scanning, RFID cards, and automated gate control. Built with ESP32 microcontrollers, it generates secure digital tickets and ensures quick, reliable, and contactless passenger access in public transport.

## Slide 3
REAL-LIFE PROBLEM
  2024 student protests in Bangladesh disrupted metro operations.
  Manual ticketing caused long queues & mismanagement.
  Lack of resilience during high-stress situations.
  Passengers, especially students, faced delays & unfair access.

## Slide 4
PROJECT PURPOSE
  Create a smart ticketing solution with ESP32 IoT devices.
  Enable secure, time-limited digital tickets (QR/RFID).
  Ensure faster passenger flow & fraud prevention.
  Reduce dependence on manual operators.

## Slide 5
CORE FEATURES
🔐 Secure One-Time Tickets (QR/RFID, 10-min validity).
🌐 Local Admin Panel (Web interface, no internet needed).
🚪 Automated Gate Control (Servo + real-time validation).
🧹 Smart Ticket Cleanup (auto-remove expired tickets).

## Slide 6
Server Integration
Gate Development
Final Integration
DEVELOPMENT STEPS
  (Conceptual)
Ticket Authentication Integration
1
2
3
4

## Slide 7
  Set up the ESP32 server in AP mode.
  Create a webpage interface with buttons to generate tickets.
  Add logic to produce secure, time-bound tickets
  Establish the server as the central ticket database.
UPDATE – 1
SERVER INTEGRATION

## Slide 8
  Connect a servo motor to act as the gate barrier.
  Install two IR sensors to detect approaching passengers.
  Programm the ESP32-S3 to control gate opening/closing.
  Gate logic linked with server: only valid tickets trigger servo movement.
UPDATE – 2
GATE DEVELOPMENT

## Slide 9
  Add ESP32-CAM to scan QR codes from tickets.
  Integrate the PN532 RFID module to read smartcards.
  Give passengers two options for entry: QR scan or RFID tap.
  Enhance gate verification by checking tickets against the server.
UPDATE – 3
TICKET AUTHENTICATION INTEGRATION

## Slide 10
  Connected a 2.4” TFT display to the server ESP32.
  Display shows QR codes directly for scanning.
  Integrated all modules: Server + Gate + ESP32-CAM + RFID + TFT.
  Completed a working prototype of a smart, standalone metro gate.
UPDATE 4
FINAL INTEGRATION

## Slide 11
IMPACT
  Faster & crowd-free access during peak hours.
  Works even in crisis situations (protests, strikes).
  Low-cost, scalable IoT solution.
  Improves resilience of public transport in Bangladesh.

## Slide 12
THANK YOU